## Slide 1
MONARCH · CONTROLS → PYTHON INTEGRATION · UPDATE 2 · 2026-07-07
From “hello” handshake to embryonic Python “brain"
Since the connectivity test (handshake): the state machine now runs in Python and matches the live LabVIEW system decision-for-decision — and along the way we found and fixed a safety gap (loss of PC heartbeat not triggering e-shutdown).
WHAT HAPPENED, IN PLAIN TERMS
▪ Brain ported & proven. The 9056’s state machine (SAFE [E-STOP]→FIRING) and warning policy now run in Python, validated in shadow mode against the live system — every state, e-stop, overrides, warning limiters (clamps).
▪ Safety gap found & fixed. The cRIO detected a lost PC but the response was never wired (original code). Now it clamps to SAFE in 5 s — proven live, pull-the-plug.
SHADOW MODE · SAME DATA, TWO BRAINS, EVERY FRAME COMPARED
IN CHARGE
LabVIEW
decides & acts
→
SHADOW
Python
sends nothing
→
COMPARED
✔ agree
every frame
THE PROOF
100%
live agreement, all 5 states
Python matched LabVIEW across every input thrown at it (limited testing only thus far)
5 s
PC connection lost → cRIO changes STATE to SAFE (E-STOP)
Tested live drop episode: PC heartbeat stops → SAFE hold → controlled step-by-step recovery; Python’s shadow agreed on every frame
144+
automated tests, on every change
all ported logic pinned by a test suite run in CI, so it can’t silently drift
PHASES A–E
A shadow brain — validated live
B command path — LabVIEW next
C operator tools
D sequencing
E warning rules
2026-07-07