## Slide 1
MONARCH · CONTROLS → PYTHON MIGRATION · UPDATE 2 · 2026-07-07
1 / 5
From “hello” to a proven brain — five days of progress
Since the July 2 connectivity test: the first supervisory state machine now runs in Python and matches the live LabVIEW system decision-for-decision — and along the way we found and fixed a real safety gap that predates this project. The safety-critical LabVIEW control still owns all hardware.
JUL 2
“Hello” link
two-way Python↔LabVIEW
connection — PASS
JUL 3
Live telemetry
real control data streams
to Python at 1 Hz
JUL 6
Migration plan
phased roadmap A–E with
safety gates at each step
JUL 7
Brain validated
Python state machine agrees
with LabVIEW live — 100% (limited testing)
JUL 7
Safety gap fixed
loss-of-PC watchdog wired
and verified
THE THREE NUMBERS THAT MATTER
100%
LIVE AGREEMENT
Python’s decisions matched LabVIEW’s across all 5 engine states and every input we could throw at it
1
SAFETY GAP CLOSED
the cRIO detected a lost PC but did nothing about it — now it safe-holds, proven with a live pull-the-plug test
144+
AUTOMATED TESTS
every piece of ported logic is pinned by tests that run on every change, so it can’t silently drift
Bottom line: the riskiest step of the migration — proving Python can faithfully reproduce the control logic against the real system — is done.

## Slide 2
MONARCH · CONTROLS → PYTHON MIGRATION · UPDATE 2 · 2026-07-07
2 / 5
The first “brain” is ported — and it matches, live
The 9056’s supervisory state machine (SAFE → STANDBY → MOTORING → IDLING → FIRING) and its warning policy were rebuilt in Python, then run in shadow mode: LabVIEW keeps deciding for real, Python decides in parallel from the same live data, and every frame is compared.
WHAT WE DID
▪ Transcribed the state machine and warning logic from the LabVIEW diagrams into plain, testable Python — pure logic, no hardware access, by design.
▪ Built a shadow-compare harness that replays every telemetry frame through the Python port and flags any decision that differs from LabVIEW’s.
▪ Exercised the whole envelope live: every state, mode walks up to FIRING, e-stop, manual overrides, and the warning clamp.
SHADOW MODE · SAME DATA, TWO BRAINS, EVERY FRAME COMPARED
IN CHARGE
LabVIEW
decides & acts
SHADOW
Python
decides, sends nothing
live data →
same decision? ✔ yes
THE RESULT
✔ 100% agreement — all 5 states, every input tested
▪ Full-envelope live sessions: override sweep 100%, e-stop 100%, mode walk 100%.
▪ Longest walk (210 frames): the actuator limiter matched 209/209; the state matched 208/209 — the single differing frame was traced to a telemetry timing artifact in the test tap, not the ported logic.
▪ Every difference found along the way is logged and dispositioned in docs/shadow-findings.md.
✓ 5/5 states
✓ e-stop
✓ overrides
✓ warning clamp
Bonus finding: shadow compare also exposed dead code — LabVIEW’s “Limited” output and two developer override switches were never wired to anything. The port is already paying for itself as an audit of the original code.

## Slide 3
MONARCH · CONTROLS → PYTHON MIGRATION · UPDATE 2 · 2026-07-07
3 / 5
Found and fixed: a safety gap older than this project
While mapping the LabVIEW code we found that the engine cRIO detected a lost control-room PC — but the response was never wired in. The alarm rang and nothing was listening. This is original-code behaviour, not something Python introduced.
BEFORE — DETECTION WITHOUT RESPONSE
▪ The watchdog computed a “PC not responding” flag…
▪ …but the flag gated nothing — no state change, no safe hold, no operator alarm.
▪ A crashed PC (LabVIEW UI or Python) would have left the engine running open-loop on stale commands.
AFTER — WIRED, SIZED, AND PROVEN
▪ The watchdog now drives the state machine: lose the PC heartbeat for 5 s and the cRIO clamps itself to SAFE — with the LabVIEW UI today or Python later.
▪ Threshold sized deliberately: 5 s ≈ 250 ticks of the ~20 ms control loop — rides out normal jitter, still trips fast.
PROVEN WITH A LIVE PULL-THE-PLUG TEST
1 PC link dropped — heartbeat stops mid-run
2 cRIO reacts alone — watchdog trips → system clamps to SAFE and holds
3 PC returns — heartbeat resumes, warning clears
4 Controlled recovery — state climbs back one step per tick — no jump to run
✔ Python’s shadow agreed on every frame of the episode
Why this matters: “if the PC dies, the engine safe-holds” was the one unverified assumption in the migration’s safety case — and the gate before Python may ever hold command authority. It is now enforced in the cRIO and demonstrated, not assumed.

## Slide 4
MONARCH · CONTROLS → PYTHON MIGRATION · UPDATE 2 · 2026-07-07
4 / 5
Built ahead: the Python side of every phase is ready
The roadmap runs A → E, each step gated by a safety review before Python gains any authority. The Python software for all five phases is written and tested — what remains is LabVIEW wiring, joint decisions, and team-supplied numbers.
A
Shadow brain
state machine + warning policy ported; validated live against the real system — 100% agreement
DONE — VALIDATED LIVE
B
Command path
Python commander built and drill-tested against a simulator; interface spec v0.2 frozen with the team; PC-loss watchdog closed
PYTHON DONE · LABVIEW NEXT
C
Operator tools
engineering CLI + an alarm that flags any live divergence between Python and LabVIEW decisions
BUILT — AWAITS PHASE B
D
Sequencing
step-by-step procedure engine + plant simulator; draft venting / purge / warm-up sequences survive randomized fault injection
BUILT — NEEDS PROCEDURES
E
Warnings & setpoints
time-based warning rules and setpoint scheduler engines, fully data-driven
BUILT — NEEDS NUMBERS
Also in place: 144+ automated tests run on every change (two Python versions); every remaining LabVIEW change is written up click-by-click so the work isn’t bottlenecked on any one person; a handoff guide covers how to continue the project.

## Slide 5
MONARCH · CONTROLS → PYTHON MIGRATION · UPDATE 2 · 2026-07-07
5 / 5
What’s next — and what we need from the team
NEXT STEPS (IN ORDER)
1
Wire the LabVIEW command path (B3)
the gateway learns to accept Python’s requests — with LabVIEW still validating every one and a single switch choosing UI or Python as the source. Fully specified, node-by-node.
2
Bench command drills (B4)
prove the failure story end-to-end: bad commands rejected, stale link means commands stop, source flips are clean, kill-Python-mid-run safe-holds.
3
First supervised bench use (Phase C)
Python drives mode requests on the bench — operator watching, LabVIEW clamp always underneath, one-command handback to the UI.
WHAT WE NEED FROM THE TEAM
▪ Operating procedures
the venting / purge / warm-up sequences are drafted from engineering judgement — they need the team’s real steps, setpoints and hold conditions (template sheets ready)
▪ Real numbers
warning thresholds, time windows and setpoint schedules are engine knowledge, not code — the engines are built and waiting for values
▪ Sign-off at each gate
every increase in Python’s authority (shadow → bench command → sequences) gets a joint review before it happens
The rule that never changes: LabVIEW/cRIO keeps the hardware, the interlocks and the safe fallback — permanently. Python only ever asks; LabVIEW checks every request; and if Python disappears, the system safe-holds. That last part is now proven, not assumed.